## Slide 1: Computer system overview
Notes: information either analog or digital needs to be converted to either a digital signal or an analog signal for transmission.
In this lecture, digital transmission only…the schemes and techniques that we use to transmit data digitally.
First, we discuss digital-to-digital conversion techniques, methods which convert digital data to digital signals.
Second, we discuss analog-to-digital conversion techniques,

## Slide 2: Need to understand computer system components
As an Operating System manages hardware resources in order to provide service to computer system users. It is therefore important to have some understanding of the underlying computer system hardware before we begin our examination of operating systems.

## Slide 3: Basic elements

## Slide 4: INSTRUCTION EXECUTION
In its simplest form, instruction processing (instruction cycle) consists of two steps:
  The processor reads (fetches) instructions from memory one at a time
  executes each instruction
Program execution consists of repeating the process of instruction fetch and instruction execution.
the program counter (PC) holds the address of the next instruction to be fetched.
Unless instructed otherwise, the processor always increments the PC after each instruction fetch so that it will fetch the next instruction in sequence.

## Slide 5: Instruction execution
The fetched instruction is loaded into the instruction register (IR).
The instruction contains bits that specify the action the processor is to take. The processor interprets the instruction and performs the required action. In general, these actions fall into four categories:
Processor-memory
Processor-I/O
Data processing:
Control: An instruction may specify that the sequence of execution be altered.
  For example, the processor may fetch an instruction from location 149, which specifies that the next instruction be from location 182. The processor sets the program counter to 182.

## Slide 6: Instruction execution
Figure shows the partial program execution, showing the relevant portions of memory and processor registers.
The program fragment shown adds the contents of the memory word at address 940 to the contents of the memory word at address 941 and stores the result in the latter location.
Three instructions, which can be described as three fetch and three execute stages, are required.
Notes: 1. The PC contains 300, the address of the first instruction. This instruction (the
value 1940 in hexadecimal) is loaded into the IR and the PC is incremented.
Note that this process involves the use of a memory address register (MAR)
and a memory buffer register (MBR). For simplicity, these intermediate registers
are not shown.
2. The first 4 bits (first hexadecimal digit) in the IR indicate that the AC is to be
loaded from memory. The remaining 12 bits (three hexadecimal digits) specify
the address, which is 940.
3. The next instruction (5941) is fetched from location 301 and the PC is
incremented.
The old contents of the AC and the contents of location 941 are added and the
result is stored in the AC.
5. The next instruction (2941) is fetched from location 302 and the PC is
incremented.
6. The contents of the AC are stored in location 941.

## Slide 7: INTERRUPTS
Virtually all computers provide a mechanism by which other modules (I/O, memory) may interrupt the normal sequencing of the processor.
Most I/O devices are much slower than the processor. Interrupts are provided primarily as a way to improve processor utilization.
Example 1Suppose that the processor is transferring data to a printer using the instruction cycle scheme. After each write operation, the processor must pause and remain idle until the printer catches up. The length of this pause may be on the order of many thousands or even millions of instruction cycles. Clearly, this is a very wasteful use of the processor.
Example 2: consider a PC that operates at 1 GHz, which would allow roughly 109 instructions per second.2 A typical hard disk has a rotational speed of 7200 revolutions per minute for a half-track rotation time of 4 ms, which is 4 million times slower than the processor.

## Slide 8: Classes of interrupts

## Slide 9: Interrupts example
The user program performs a series of WRITE calls interleaved with processing. The solid vertical lines represent segments of code in a program. Code segments 1, 2, and 3 refer to sequences of instructions that do not involve I/O. The WRITE calls are to an I/O routine that is a system utility and that will perform the actual I/O operation. The I/O program consists of three sections:
  A sequence of instructions, labeled 4 in the figure, to prepare for the actual I/O operation. This may include copying the data to be output into a special buffer and preparing the parameters for a device command.
  The actual I/O command. Without the use of interrupts, once this command is issued, the program must wait for the I/O device to perform the requested function (or periodically check the status, or poll, the I/O device). The program might wait by simply repeatedly performing a test operation to determine if the I/O operation is done.
  A sequence of instructions, labeled 5 in the figure, to complete the operation. This may include setting a flag indicating the success or failure of the operation.

## Slide 10: Interrupts example
The dashed line represents the path of execution followed by the processor; that is, this line shows the sequence in which instructions are executed. Thus, after the first WRITE instruction is encountered, the user program is interrupted and execution continues with the I/O program.
After the I/O program execution is complete, execution resumes in the user program immediately following the WRITE instruction.
Because the I/O operation may take a relatively long time to complete, the I/O program is hung up waiting for the operation to complete; hence, the user program is stopped at the point of the WRITE call for some considerable period of time.

## Slide 11: Interrupts example
With interrupts, the processor can be engaged in executing other instructions while an I/O operation is in progress.
As before, the user program reaches a point at which it makes a system call (WRITE call). The I/O program that is invoked in this case consists only of the preparation code and the actual I/O command. After these few instructions have been executed, control returns to the user program. Meanwhile, the external device is busy accepting data from computer memory and printing it. This I/O operation is conducted concurrently with the execution of instructions in the user program.
When the external device becomes ready to be serviced, that is, when it is ready to accept more data from the processor, the I/O module for that external device sends an interrupt request signal to the processor. The processor responds by suspending operation of the current program; branching off to a routine to service that particular I/O device, known as an interrupt handler; and resuming the original execution after the device is serviced.
Note that an interrupt can occur at any point in the main program, not just at one specific instruction.

## Slide 12: Transfer of Control via Interrupts

## Slide 13: Instruction Cycle with Interrupts
To accommodate interrupts, an interrupt stage is added to the instruction cycle.
In the interrupt stage, the processor checks to see if any interrupts have occurred, indicated by the presence of an interrupt signal.
If no interrupts are pending, the processor proceeds to the fetch stage and fetches the next instruction of the current program. If an interrupt is pending, the processor suspends execution of the current program and executes an interrupt-handler routine.
The interrupt-handler routine is generally part of the OS, that determines the nature of the interrupt and performs whatever actions are needed.

## Slide 14: Interrupt Processing

## Slide 15: Multiple Interrupts
An interrupt occurs while another interrupt is being processed
e.g. receiving data from a communications line and printing results at the same time
Two approaches:
disable interrupts while an interrupt is being processed
use a priority scheme

## Slide 16: Multiple Interrupts

## Slide 17: Multiple Interrupts

## Slide 18: THE MEMORY HIERARCHY
The design constraints on a computer’s memory can be summed up by three questions:
How much? . If the capacity is there, applications will likely be developed to use it.
How fast? easier to answer. To achieve greatest performance, the memory must be able to keep up with the processor.
How expensive? For a practical system, the cost of memory must be reasonable in relationship to other components.

## Slide 19: THE MEMORY HIERARCHY
there is a trade-off among the three key characteristics of memory: namely, capacity, access time, and cost.
  Faster access time, greater cost per bit
  Greater capacity, smaller cost per bit
  Greater capacity, slower access speed
The way out of this dilemma is to not rely on a single memory component or technology, but to employ a memory hierarchy.
A typical hierarchy is shown. As one goes down the hierarchy, the following occur:
  Decreasing cost per bit
  Increasing capacity
  Increasing access time
  Decreasing frequency of access to the memory by the processor
The key to the success of this organization is the decreasing frequency of access at lower levels.

## Slide 20: locality of reference principle
During the course of execution of a program, memory references by the processor, for both instructions and data, tend to cluster.
Programs typically contain a number of iterative loops and subroutines. Once a loop or subroutine is entered, there are repeated references to a small set of instructions.
Similarly, operations on tables and arrays involve access to a clustered set of data bytes. Over a long period of time, the clusters in use change, but over a short period of time, the processor is primarily working with fixed clusters of memory references.

## Slide 21: Secondary memory
Also referred to as auxiliary memory
  external
  nonvolatile
  used to store program and data files
  Example is Hard Disk
A hard disk is also used to provide an extension to main memory known as virtual memory
Additional levels can be effectively added to the hierarchy in software. For example, a portion of main memory can be used as a buffer to temporarily hold data that are to be read out to disk. Such a technique, sometimes referred to as a disk cache

## Slide 22: Cache memory
Invisible to the OS
Interacts with other memory management hardware
Processor must access memory at least once per instruction cycle
Processor execution is limited by memory cycle time
Exploit the principle of locality with a small, fast memory

## Slide 23: Cache memory